## Slide 1: CAER Safety Summit 2021 Valero Fatality – Lessons Learned
Presented by Nick Plurkowski, United Steelworkers Local 5

## Slide 3
Was this incident preventable?

## Slide 4
Here are some definitions for the following terms:
Confined Space / Permit Required Confined Space
Attendant or “Hole Watch”
Fall Protection / Fall Prevention / Fall Arrest
Hazardous Atmosphere / IDLH / Ventilation
Rescue
https://www.dir.ca.gov/title8/5157.html

## Slide 5: Confined Space
Confined space means a space that:
(1) Is large enough and so configured that an employee can bodily enter and perform assigned work; and
(2) Has limited or restricted means for entry or exit (for example, tanks, vessels, silos, storage bins, hoppers, vaults, and pits are spaces that may have limited means of entry.); and
(3) Is not designed for continuous employee occupancy.

## Slide 6: Permit Required Confined Space
Permit-required confined space (permit space) means a confined space that has one or more of the following characteristics:
(1) Contains or has a potential to contain a hazardous atmosphere;
(2) Contains a material that has the potential for engulfing an entrant;
(3) Has an internal configuration such that an entrant could be trapped or asphyxiated by inwardly converging walls or by a floor which slopes downward and tapers to a smaller cross-section; or
(4) Contains any other recognized serious safety or health hazard.

## Slide 7: Attendant – “Hole Watch”
Attendant means an individual stationed outside one or more permit spaces who monitors the authorized entrants and who performs all attendant's duties assigned in the employer's permit space program.

## Slide 8: Fall Protection Systems
Fall Protection Systems There are 2 basic types of fall protection systems:
  Passive Systems - Fall Prevention - Guardrails, safety nets, floor covers, catch platforms, etc.
  Active Systems - Personal Fall Protection - Safety belts and body harnesses

## Slide 9: Hazardous Atmosphere
Hazardous atmosphere means an atmosphere that may expose employees to the risk of death, incapacitation, impairment of ability to self-rescue (that is, escape unaided from a permit space), injury, or acute illness from one or more of the following causes:
(1) Flammable gas, vapor, or mist in excess of 10 percent of its lower flammable limit (LFL);
(2) Airborne combustible dust at a concentration that meets or exceeds its LFL;
(3) Atmospheric oxygen concentration below 19.5 percent or above 23.5 percent;
(4) Atmospheric concentration of any substance for which a dose is published in Group 14 for Radiation and Radioactivity or a permissible exposure limit is published in section 5155 for Airborne contaminants and which could result in employee exposure in excess of its dose or permissible exposure limit;
(5) Any other atmospheric condition that is immediately dangerous to life or health.

## Slide 10: IDLH
Immediately Dangerous to Life or Health (IDLH) means any condition that poses an immediate or delayed threat to life or that would cause irreversible adverse health effects or that would interfere with an individual's ability to escape unaided from a permit space.

## Slide 11: Ventilation
Continuous forced air ventilation shall be used, as follows:
  a. An employee may not enter the space until the forced air ventilation has eliminated any hazardous atmosphere;
  b. The forced air ventilation shall be so directed as to ventilate the immediate areas where an employee is or will be present within the space and shall continue until all employees have left the space;
  c. The air supply for the forced air ventilation shall be from a clean source and may not increase the hazards in the space.

## Slide 12: Rescue
Rescue service means the personnel designated to rescue employees from permit spaces.

## Slide 14
R-702

## Slide 15: R-702 Overflow Well located inside R-702

## Slide 16: PRCS #1 R-702
PRCS # R-702
Overflow
Well

## Slide 17: Camera 1-outside to monitor Entrants & PPE
Camera 2-
inside to monitor Entrants working

## Slide 18: Fall Protection above ladder (~50 ft to bottom)

## Slide 19: Gas Monitor (only setup to monitor R-702 entrance)

## Slide 20: Ventilation
Ventilation
(not reaching the bottom, low flow)

## Slide 21: Gas Testing (representative sample?) (ongoing???)

## Slide 22: Weld job was to happen at the bottom of the Overflow Well on a nozzle…

## Slide 23: Argon hose ran to job as part of Weld equipment

## Slide 24: Weld job couldn’t happen until excess refractory was cleaned up at bottom

## Slide 25: Argon leaking

## Slide 26: Argon accumulating (IDLH)

## Slide 27: Rescue Efforts ~20min response No Badge-In for ~10 rescue personnel No PRCS (#2) identified No Gas Test (=IDLH) No Respiratory Protection (SCBA) Used Fall Protection No Rescue Team

## Slide 28
Was this incident preventable?

## Slide 29: A worker gets dizzy in the R-702 Overflow Well
Nov. 19th 2021

## Slide 30: Luis Gutierrez is overcome by an IDLH atmosphere
Nov. 12th 2021 (Nightshift)

## Slide 31: A worker gets dizzy in the R-702 Overflow Well
Nov. 12th 2021 (Dayshift)

## Slide 32: CalOSHA responds to Total Safety’s inquiry about their system being CA compliant…
August 18th 2021

## Slide 33: United Steelworkers at the Chevron Richmond Refinery participate in a MOC to allow Total Safety’s program
They pushed back April / May 2021

## Slide 34
Timeline:
April / May 2021 – USW pushes back against Total Safety at Chevron Richmond
August 18, 2021 – CalOSHA issues a memo to Total Safety saying the program doesn’t meet Regulation
November 12, 2021 – Near Miss of a worker getting dizzy in the R-702 Overflow Well (Dayshift)
November 12, 2021 – Luis Gutierrez is overcome by an IDLH atmosphere in the R-702 Overflow Well (Nightshift)
November 19, 2021 – Near Miss of a worker getting dizzy in the R-702 Overflow Well

## Slide 35
Was this incident preventable?

## Slide 36: Learnings
Employee Participation
Stop Work Authority
Near Misses reported, investigated and mitigated immediately
Proper Attendant / “Hole Watch” program
Leaking hoses (any equipment) be destroyed (not re-used)
Rescue Plans be written out & verified by those to be rescued
Rescue equipment with a crank
Proper gas testing
Proper gas monitoring
Proper Ventilation
Proper PRCS identification
Safety Culture

## Slide 37: CAER Safety Summit 2021 Valero Fatality – Lessons Learned
Presented by Nick Plurkowski
United Steelworkers Local 5
(925) 451-5564
nplurkowski@usw5.org